## Slide 1
Reliability Issues
of
3-Phase Locomotives
14-15 Feb, 2019
<number>

## Slide 2: ISSUES OF C-DAC TCN VCU

## Slide 3: Performance of M/s. ABB make C-DAC VCU
SN | Item | Action plan | Remark
1. | S/w mismatch & Life sign missing | Software need to be modified. | One loco at ELS/RPM is running with modified software. Performance is under watch. PDC: 31.03.19.
2. | Cab redundancy issue | Cab redundancy in C-DAC based VCU to be provided in line with MICAS VCU. | C-DAC is working on this. PDC – 20.02.2019.
3. | Display issue | Aux. Converter failure data doesn’t get displayed in DDU. | Shall be discussed during meeting at ELS/HWH

## Slide 4: Performance of M/s. ABB make C-DAC VCU
SN | Item | Details
4. | Error messages | Following error messages getting logged in C-DAC VCU on regular basis (& sometimes TBG gets isolated):- SLG1:0137-MC2 Boggie-1 Isolated SLG2:0129-Dist In speed sensor Motor-3 SLG1:0017-Conv Coolant flow < Limit SLG1:0107-Dist.In speed sensor Motor-1 SLG1:0118-Dist In speed sensor Motor-2 SLG1:0136-MC1 Boggie-1 Isolated
5. | Unreliable indication | Trafo, SR & AUX CON parameter (voltage, current , frequency & pressure) displayed in DDU are inconsistent & unreliable for trouble shooting & indication point of view.

## Slide 5: Performance of M/s. CGL make C-DAC VCU
SN | Item | Details
1. | Software issues | Issues yet to be resolved Life sign missing from all Processors Wrong sensing of Speed : FLG1:0020- Emergency Vigilance Brake Loco not moving due to TE/BE reads “ZERO” Life sign missing from various subsystem and processor card. Non formation of multiple unit with same cab i.e. cab1 to cab1 and cab2 to cab2. Wrong panto sequence while activating locomotive from Cab-2 (Pantograph of unoccupied cab of both the locos rising), while it was normal from cab-1. Non- display of Node information of Master loco in the DDU of slave loco. Display of spurious messages in the DDU-‘Angle Transmitter fail, More than one cab occupied, Emergency stop- shut down, Train bus disturbance slave, Simulation fault etc. ……………

## Slide 6: Performance of M/s. CGL make C-DAC VCU
SN | Item | Details
1. | Software issues | Issues yet to be resolved Tripping of DJ and simultaneous dropping of pantograph in case of ‘Low/No OHE voltage’ or isolation of any subsystem. Non-display of Primary current (Ipri) in DDU. Wrong display of value (20%) of 0101-XangTrans (FLG-1) at ‘0’ position of Throttle. Non-working of Unloader valves of Main compressor during closing of DJ, in case of MR pressure < 8 kg/cm2 caused excess current drawn by the main compressor thereby sometimes tripping of MCBs of Main compressor. In fault messages, Date & Time of some messages get re-setted (i.e. 1.1.1970). In error log some fault messages logged as error undefined. Individual TM isolation is not addressed properly. Wheel diameter setting feature is not available.

## Slide 7: Performance of M/s. CGL make C-DAC VCU
SN | Item | Details
2. | Cab redundancy feature not incorporated till date. | Cab redundancy as per MICAS VCUs need to be implemented.
3. | AFL not working. | AFL not working in standstill condition and also in running condition in some locos
4. | VCB stuck-up. | Messages comes after passing neutral section.
5. | MCB-100 trip message not Pop-up on DDU | MCB-100 (Battery charger MCB) trips and message not Pop-up on DDU. Due to this battery gets run down on line.

## Slide 8: Performance of M/s. CGL make C-DAC VCU
SN | Item | Details
6. | Message "earth fault trafo or motor" logged in data with Traction Bogie isolated. | Modified Software loaded but problem not resolved.
7. | Message display on DDU | Motor isolation popup message is logged in DDS but not displayed on DDU.
 |  | BUR failure data doesn’t get displayed in DDU.

## Slide 9: Performance of M/s. BHEL make C-DAC VCU
SN | Item | Details | Remark
1. | TM isolation from DDU is possible only from CAB-1 | In BHEL TCN Locos, TM isolation from DDU is possible only from CAB-1. From CAB-2 TM isolation not possible from DDU. | BHEL has stated that they will study the issue and revert back by 20.02.2018.
2. | Frequent failure of train bus communication in MU operation | Frequent failure of train bus communication in MU operation of MICAS based system with IGBT BHEL traction converter. The failures are transient but repetitive in nature. | BHEL to study the issue and submit the action plan.

## Slide 10: Performance of M/s. BHEL make C-DAC VCU
SN | Item | Details | Remarks
3. | Multi operation failure | Multi operation failure in BHEL TCN loco due to reasons like tripping of slave loco & panto lowered, traction not allowed in master & slave loco. | Trials in different combinations of MU gateway successful in ELS/VSKP.
4. | Harmonic current high. | Trial has been conducted at ELS/VSKP in loco no. 31967 on 24.01.19. | Performance under watch.

## Slide 11: TCN (C-DAC) VCU – Issues Reported by SR
SN | Issues | Fault logged/ Remarks | CGL | ABB
1 | Bogie isolation due to software mismatch | FLG1:0084 - SLG-2 S/W version mismatch. | √ | √
 |  | FLG1:0082 - Master def. bogi2 mismatch. |  | 
2 | Battery charger stops working. | BUR2:0020 - Bat. Charge current below 10A (Battery voltage 99V). | √ | ×
 |  | BUR3:0016 - Bat. Charge current below 10A (Battery voltage 414V). |  | 
3 | wrong sensing of speed, BP and OHE. | FLG: 0037 - S/R interlock - Loco brake. | √ | ×
4 | Hardware Failure messages. | SLG : 0002 - Analog input slot T defective. | × | √
 |  | FLG: 0048 - Timeout peri. Test end B1 and TEC hardware failure. |  | 
5 | Undefined Error | Error Undefined - 0055 | × | √
 |  | Error Undefined - 0089 |  | 

## Slide 12: Performance of M/s. BTIL make Converters (IGBT)
<number>

## Slide 13: Performance of M/s. BTIL make Traction Converter
Notes: <number>

## Slide 14: Performance of M/s. BTIL make Traction Converter (SHED WISE)
Notes: <number>

## Slide 15: Performance of M/s. BTIL make Traction Converter
SN | Item | Details | Remark
1 | Failures of Power Modules | Release of new SW version 218T01BT & 318T01BT that limits the max allowed current when the coolant flow is suboptimal during the ramp up of the aux converter. M/s BTIPL has proposed to replace a pipe in the converter cooling circuit that has an orifice of 18mm diameter with one that uses a larger orifice with 21.5.mm diameter to increase the coolant flow rate from 176 LPM to 237 LPM. | Modified software installed in – 130 locos Balance – 40 PDC – 28.02.19. RDSO has cleared to replace the cooling circuit with increased orifice of 21.5 mm in 25 locomotives.

## Slide 16: Performance of M/s. BTIL make Traction Converter
SN | Item | Details | Remark
2 | Main power OFF due to ‘FLG-1 time out DC link circuit charge’ | Addressed in new SW version 218T01BT & 318T01BT that limits the max allowed current when the coolant flow is suboptimal during the ramp up of the aux converter. | Modified software installed in – 130 locos Balance – 40 PDC – 28.02.19.
3 | DC link overvoltage during regeneration. | The problem was addressed in previous software version; however the fault messages are still being reported. Firm has been advised to re-look. | The matter shall be discussed in reliability meeting on 14/15.02.19 at ELS/HWH.
Notes: <number>

## Slide 17: Performance of M/s. BTIL make Traction Converter
SN | Item | Details
4. | Logging of spurious messages | ELS/BRC reported following: In loco 30480: CON1: 311 Trac. Mot.2 Temp. implausible. CON1/2: PSU for DCUM implausible. In loco 30470: “CON1:204 A627 PSU for DCUM3 implausible”, “CON1:203 A625 PSU for DCUM2 implausible”, “CON1:202 A623 PSU for DCUM1 implausible”, “CON1:201 A621 PSU for PCUL implausible” In loco 30474 : TM2 Bogie-1 isolate without any failure message con1 M2 pulsing not started DCUM1 or cabling faulty DCUM3 or cabling faulty- Bogie 1 got isolated Main power got off without any message

## Slide 18: Performance of M/s. BTIL make Traction Converter
SN | Item | Details
4. | Logging of spurious messages (contd) | In loco 30486 : bogie isolated due to following messages CON2: comm.. Loss to DCUM1, DCUM2, DCUM3 & DCUL. CON2: PSU OFF relay feedback fault. Dist. Redundant VCI2 Dist. Comm. CON2 VCI VCI2 : Amp2 isolate

## Slide 19: Performance of M/s. BTIL make Traction Converter
SN | Item | Details | Remark
5. | Isolating cock in cooling circuit | Isolating cock has not been provided in cooling circuit of traction converter. Required to incorporate the same to prevent drainage of coolant during radiator/converter replacement. | Further decision will be taken to provide the same on requirement evaluation.

## Slide 20: Performance of M/s. BTIL make Propulsion System
SN | Item | Details | Remark
1. | Issues common with the traction converter | Limited approval for 12 locos for trial was given. It will address following issues: Addressing IGBT failure issues. MU functionality Hotel load integration functionality | PDC for regular cut-in 20.02.19.
2. | Corruption of wheel diameter due to software problem. | As per M/s BT, the wheel diameter data is being stored in NV memory which get corrupted very easily. They are planning to move this data to internal memory of DCU cards. | M/s BT to give the action plan.

## Slide 21: Performance of M/s. BTIL make Propulsion System
SN | Item | Details | Remark
3. | Catenary voltage out of limits. | The propulsion software has been drawn as per old MICAS software. The changes related to OHE voltage limit need to be implemented. | M/s BT to give the action plan.
4. | CCUO: 0231-UPRIM Sensing Ckt Flt SPIF1 logged and subsequently main power off. | Under investigation. | M/s BT to give the action plan.
5. | Relevant variables always are missing in DDS data. | In DDS environment data relevant variables always are missing. i.e. in error log pertaining to OHE voltage, OHE voltage field is missing. & same is the case with other error messages. | BTIL has to take corrective action

## Slide 22: Performance of M/s. BTIL make Propulsion System
SN | Item | Details | Remark
6. | Issues in propulsion system faced by ELS/HWH | Motors are getting isolated frequently with message ‘speed sensor single channel faulty & M1/M2/M3 switching command feedback failure. Messages are being logged, ‘L: Pantograph bouncing’ then all BUR remains idle or in recovery stage which leads sensing ‘low coolant pressure’ by both traction converters. During self-testing sometimes Traction bogie getting isolated without any message. Protective shut down due to ‘MVB pull wire from other DCU active’. TMs are getting isolated without sufficient back ground data in DDS. | M/s BT to give action plan

## Slide 23: Performance of M/s. BTIL make Propulsion System
SN | Item | Details | Remark
7. | Other issues | Sometimes even in shed during loco checking suddenly VCB tripped, PT got down & after some time PT got raised by itself & following disturbance messages logged. CCUO:0198- Catenary Voltage out of Limits. CCUO:0183-Power reduction line voltage L: Power limitation 1 active (PLine) L: Pantograph bouncing | BT has to take corrective action and to submit the action plan.
 |  | On AUX CON data most of the time no fault is getting logged. | 
 |  | Traction converter is getting isolated without any message and with message ‘L charging resistor too hot’. | 

## Slide 24: Performance of M/s. BTIL make Propulsion System
SN | Item | Details | Remark
7. | Other issues (contd) | When any fault occurs dds is showing only the latest instant of fault occurrence and older ones are storing as counts. So Lp is unable to check the sequence of fault occurrence. When ZTEL is operated Traction is limited to only 84 KN. | BT has to take corrective action and to submit the action plan.

## Slide 25: Performance of M/s. BTIL make Propulsion System
SN | Item | Details | Remark
7. | Other issues (contd) | Sometimes even in shed during loco checking suddenly VCB tripped, PT got down & after some time PT got raised by itself & following disturbance messages logged. CCUO:0198- Catenary Voltage out of Limits. CCUO:0183-Power reduction line voltage L: Power limitation 1 active (PLine) L: Pantograph bouncing | BT has to take corrective action and to submit the action plan.
 |  | On BUR data most of the time no fault is getting logged. | 
 |  | Traction converter is getting isolated without any message and with message ‘L charging resistor too hot’. | 

## Slide 26: Performance of M/s. BTIL make TCN VCU
SN | Item | Details
1. | Shunting mode message is logging only for the first instant. | ELS/RPM has informed that these problems are being faced in M/s BTIPL make propulsion system.
2. | Traction not allowed with applied brakes messages logging even at throttle ‘0’position. | 
3. | Shunting speed is available up to 20 kmph but usually it is 15 kmph. | 
4. | Filter contactors are not operated when note is shifted from 596 o 590. Also when throttle is 0 but speed is not 0, loco shows node 590. | 

## Slide 27: Performance of M/s. ABB make Converters (IGBT)
<number>

## Slide 28: Performance of M/s. ABB make Traction Converter
<number>
Notes: <number>

## Slide 29: Performance of M/s. ABB make Traction Converter (SHED WISE)
<number>
Notes: <number>

## Slide 30: Performance of M/s. ABB make Traction Converter
SN | Item | Details | Remark
1. | Failure of PEBB module | ABB has indicated that some issues for failure of IGBT modules have been identified and resolved in SW ver-40. | Regular use of Software ver-40 has been accorded in WAP-5 locos. Software downloaded in 4 locos of of 5 in GZB and 2 out of 8 in BRC. Performance under watch.
2. | Software malfunctioning, TE becomes 0. | This issue will be resolved in SW ver-40. | 

## Slide 31: Performance of M/s. ABB make Traction Converter
SN | Item | Details | Remark
3. | New software Issues: Issue of ‘LC Overcurrent’ | Maximum issues are reported of LC and MC Overcurrent. Issues are particularly with 1500 Amp IGBT. | Issue with the 1500 A new Hitachi make IGBTs. Firm carrying trial with version – 40. Software shall be ready by 20.02.2018.
4. | Coolant replacement activities | As per RDSO SMI-325. | Total locos to be modified: 70 Locos modified: 56 Locos to be modified: 14 PDC – 28.02.19.
5. | Loco resetting issue | When loco resetted using VCU reset then Traction will resume only after speed becomes zero | Corrective action to be submitted.

## Slide 32: Performance of M/s. ABB make Aux. Converter
<number>
Notes: <number>

## Slide 33: Performance of M/s. ABB make Aux. Converter (SHED WISE)
<number>
Notes: <number>

## Slide 34: Performance of M/s. ABB make Aux. Converter
SN | Item | Details | Remark
1. | Failure of IGBT module | Failure of IGBT modules of BUR. Earthing to be done as per GTO locomotives. | Total locos to be modified: 39 Locos modified: 32 Locos to be modified: 7 BRC-30076, TKD-31777, RPM-30479, TKD-31405, 31406, 31477, 31481. PDC: 15.03.19.
2. | Battery charger failure | Auxiliary converter failure due to CHBA stops working sometimes & load shifting doesn’t take place from BUR-3. | ABB has to take corrective action.
 |  | Auxiliary converter failure due to CHBA DC link capacitor burst/CHBA defective, Chopper circuit burnt & input fuse melt. | Shall be discussed during meeting at ELS/HWH
 |  | Battery charger not working at times. | Software updated and loaded. Under observation.

## Slide 35: Performance of M/s. CGL make Converters (IGBT)
<number>

## Slide 36: Performance of M/s. CGL make Traction Converter

## Slide 37: Performance of M/s. CGL make Traction Converter (SHED WISE)

## Slide 38: Performance of M/s. CGL make Traction Converter
SN | Item | Action plan | Remark
 | Failure of power module & their connector | CGL has proposed to modify the modules with bus-bar type arrangement in place of existing arrangement. | Total locos to be modified: 69 Locos already modified: 42 Locos still to be modified: 27 (BNDM-8, GMO-10, LDH-01, NKJ-07, KZJ-01) The rate of modification is too slow. M/s CGL to expedite the same at the earliest. PDC – 31.03.2019

## Slide 39: Performance of M/s. CGL make Traction Converter
SN | Item | Action plan | Remark
2. | Software issues | Issues with Software version 0023: Isolation of Traction bogie 1 & 2 with message ‘Time out NSC pulse Bogie1/ Bogie2’. Some times after MCE OFF/ON isolation of Traction bogie 1 and 2 with message ‘Time out ALG test2 end Bogie1/Bogie2’. Vbus Max | Modified software ver. 25 beta 04 provided in locomotive no. 39001, 39002, 39004 & 30680 of ELS/RPM Performance is under monitor.

## Slide 40: Performance of M/s. CGL make Traction Converter
SN | Item | Action plan | Remark
3. | Issues with UTIZEN CPU electronics | To reduce the booting time. The problem of isolation of motors/bogie, non-logging of fault data in line with the VCU data could not be set right so far on converters with UTIZEN electronics. CGPISL is having 14 locomotives converters of UTGEN type. | M/s CGL has been impressed upon to replace the UTIZEN electronics with new VEGA electronics as there are several software issues which could not be solved. M/s CGL will revert back by 15.02.2019.

## Slide 41: Performance of M/s. CGL make Traction Converter
SN | Item | Action plan | Remark
4. | TE / BE reduces to zero | For this CGPISL requires uploading the solution in two locomotives at ELS/RPM for few days to collect the data and tuned the parameter. | Modified software has been uploaded in loco nos. 30680, 39001, 39002 & 39004 of ELS/RPM. Performance is under observation.
5. | Failure of modified X24 Card (Analogue I/0 card). | Investigation report along with action plan to be submitted. | M/s CGL stated that they will submit the same by 20.02.2019.

## Slide 42: Performance of M/s. CGL make Traction Converter
SN | Item | Action plan | Remark
6. | Repeated failure of balancing resistor | The issue is with Kiyosh make resisters. The failure is due to overheating of resister and its outer cover is getting cracked. M/s CGL shall replace Kiyosh make resisters with HVR Pentagon make resistors. | Resistor with increased diameter from 54mm to 80mm has been provided in one loco no. 30693 of ELS/RPM. 4 locos are balance. Two resistors of 1.95K Ohm each in cascaded in place of single resistor (3.91K Ohm) has been added in two locos no. 30577 & 39000 of ELS/RPM. 3 more locos are balance for this modification. PDC – 28.02.2019 Further decision will be taken after satisfactory performance.

## Slide 43: Performance of M/s. CGL make Traction Converter
SN | Item | Action plan
7. | Sludge formation even after flushing & filling up of coolant as per SMI-0325 | Formation of sludge has been experienced in 3 locomotives (Loco No. 31739, 31742 & 31917) by ELS/BNDM even after replacement of coolant of M/s Chemtex make with coolant of M/s Clariant make as per RDSO SMI 325..
8. | Rampant failures of Speed sensors of M/s Jaquet make | Rampant failures of Speed sensors of M/s Jaquet & M/s Laxven make are being experienced.
9. | Isolation of both bogies. | Both bogies are getting isolated without fault messages at times.

## Slide 44: Performance of M/s. CGL make Traction Converter
SN | Item | Details
10. | Other Software issues | When any motor gets isolated, corresponding popup message of isolation does not get displayed. However, message is logged in DDS. Spurious messages of “Info: SLG has received a shutdown command” messages are getting logged in SR data. When transformer oil pump MCB is tripped manually, then message of oil temperature high appears instantly without increase in oil temperature. VCB stuck-up messages are more frequently coming after passing neutral section. SR isolation due to multiple life sign missing from MVB is frequent. Both bogies are getting isolated without fault messages at times.

## Slide 45: Performance of M/s. CGL make Aux. Converter
Notes: <number>

## Slide 46: Performance of M/s. CGL make Aux. Converter (SHED WISE)
Notes: <number>

## Slide 47: Performance of M/s. CGL make Aux. Converter
SN | Item | Action plan | Remark
1. | Modification in the INVCC and CCPU card. | Still card failures are there. The card failures are with message battery charger current less than 10 Amp and BUR current greater than maximum and inverter fault. | Firm has modified the software and provided modified software in Five locomotives each at four locations RPM, TKD, HWH and GMO. Locomotive numbers are as given below. HWH- 30305, 30506, 30454, 30503, 30455. RPM - 30679, 30680, 39004, 30678, 30675 GMO - 31267, 37047, 31316, 32153, 32074, 31596, 32152 TKD - 30653, 30683, 30451, 30637, 32200, 31548.
2. | BUR current greater than Maximum still to be resolved. | CGL has modified software and downloaded in five (05) locos each at ELS/HWH, RPM, GMO & TKD. Performance under watch. | 
3. | ‘Battery charger current below 10A is still unresolved. | CGL has modified software and downloaded in five (05) locos each at ELS/HWH, RPM, GMO & TKD. Performance under watch. | 

## Slide 48: Performance of M/s. CGL make Aux. Converter
SN | Item | Details | Remark
4. | Auxiliary Converter over current issue | After neutral section, the frequency ramps down and takes near about 10 seconds to reach zero frequency. If driver close DJ within 5 seconds before frequency coming down below 35 Hz, auxiliary converter over current message appears and immediately DJ trips. | CGPSIL has to study the issue and propose the solution by 20.02.2019.
5. | MCB-100 trip message pop-up issue | MCB-100 (Battery charger MCB) trips and message not Pop-up on DDU. Due to this battery gets run down on line. | CGL to submit the investigation report and action plan.

## Slide 49: Performance of M/s. CGL make Aux. Converter
SN | Item | Details
6. | Other issues | Date and time format & value gets corrupted in fault data of AUX CONV.
 |  | BUR parameters are either not available or are erratic & unreliable in DDU.
 |  | High failure rates of the auxiliary machines

## Slide 50: Performance of M/s. Medha make Propulsion system
<number>

## Slide 51: Performance of M/s. Medha make Propulsion

## Slide 52: Performance of M/s. Medha make Propulsion (SHED WISE)

## Slide 53: Performance of M/s. Medha make Propulsion system
SN | Item | Action plan | Remark
1. | Bursting of capacitor: In locomotive no 30553 at ELS/TATA the DC link capacitor burst, which led to failure of Power module. | Firm has informed that they have sent the failed DC link capacitor to Electronicon (Italy) and waiting for detailed investigation report. | M/s Medha stated that they have received Analysis Report from M/s. Electronicon, but not satisfied with their report. M/s Medha requested Electronicon to re-examine and submit the root cause analysis. PDC – 15.02.2019

## Slide 54: Performance of M/s. Medha make Propulsion system
SN | Item | Action plan | Remark
2. | Interoperability of MU units: | Multi-operation of locomotive of MEDHA with propulsion of BHEL to be done. Firm advised to visit the ELS/LGD with M/s BHEL and test the Multi-operation at the earliest. | MU operation with C-DAC VCU and M/s Medha make VCUs to be done. M/s Medha requested to allot the locomotive having C-DAC VCU along with protocol details.
3. | Harmonic filter getting isolated | In case of isolation of any Traction converter automatically / manually, filter current increases and ultimately Harmonic filter getting isolated. | Software updated Locomotives working without any issues as on date. Software updated in 46 Locos out of 113. Balance – 67 PDC: 28.02.2019.

## Slide 55: Performance of M/s. Medha make Propulsion system
SN | Item | Action plan | Remark
4. | There are several cases of isolation and recovery of subsystem automatically due to transient troubles. | Updated software have been provided in 10 Locomotives 37001/Ajni, 30547/SRC, 31930/TATA, 31902/TATA, 31920/TATA, 30558/SRC, 30149/GZB, 30700/SRC, 30595/LGD and 30649/GZB. | Concerned Railways to give feedback.
5. | Message “Converter oil pressure not ok” does not store in DDS and whenever coolant temperature goes out of limit then directly “Converter oil temperature too high” message appears and the respective SR or Bogie gets isolated. |  | 
Notes: <number>

## Slide 56: Performance of M/s. Medha make Propulsion system
SN | Item | Details
6. | Bogie isolation | Bogie isolated on line instead of individual TM-4 isolation.
7. | Initial TE of 18% (40KN) observed in WAP5 locos. | All locos equipped with M/s MEDHA make propulsion reported with same problem by ELS/BRC.
8. | DC link over voltage | There are several messages like ‘DC link over voltage’ which are not available in DDS but available in display unit. There are other such messages. Complete list needs to be prepared.
9. | Earth fault sensing ckt. | Extra ‘earth fault sensing ckt.’ in each Aux. converter is provided which causes protective shut down of Aux. Conv. In case of bonding of Scavenger leading to concerned BUR OFF and automatically transferring load to other BUR which also senses earth fault and gets isolated and due to isolation of both conv. ‘Main power gets OFF’.

## Slide 57: Performance of M/s. Medha make Propulsion system
SN | Item | Action plan
10. | Harmonic filter getting isolated | In case of isolation of any Traction converter automatically / manually, filter current increases and ultimately Harmonic filter getting isolated.
11. | “OHE voltage out of range message” not appearing in DDS | “OHE voltage out of range message” not appearing in DDS and loco does not trip. Due to OHE voltage out of range inverter pulsing stopped and further throttle not responding.
12. | SR gate unit power supply MCB tripping | SR gate unit power supply MCB (20 amps) tripping causing Traction bogie isolate.
13. | Wrong display of energy regeneration | In place of Energy consumption, Display showing Energy regeneration in all newly received WAP7 locomotives.

## Slide 58: Performance of M/s. BHEL make Converters (IGBT)
<number>

## Slide 59: Performance of M/s. BHEL make Traction Converter
<number>

## Slide 60: Performance of M/s. BHEL make Traction Converter (SHED WISE)
<number>

## Slide 61: Performance of M/s. BHEL make Traction Converter
SN | Item | Action plan | Remark
1 | Power Module Failures | Protection level of monitoring time has been modified for from existing 750ns to 1000ns. The vulnerable component shall be replaced with improved rating components. Failure of power modules is very high. Maximum failures due to Tmax, SEPL, Start Err Top/Bottom phase. | BHEL informed that higher rated MOSFET driver introduced from Oct 2017 and higher rated MOSFET introduced in gate drivers from June 2018 in regular production to improve the reliability of gate driver after usage in converters at Kazipet. Software ver. 774 with increased timing parameter for SEPL max detection introduced loaded in all 347 Locos. BHEL should look into the problem afresh.

## Slide 62: Performance of M/s. BHEL make Traction Converter

## Slide 63: Performance of M/s. BHEL make Traction Converter
SN | Item | Action plan | Remark
3. | Reduction of TE/BE with no DDS at higher speed. | Occurring due to loss of Panto contact with OHE for more than 45ms. This has come to light after analyzing the data of loco 30129 of ELS/GZB where this problem occurred. BHEL was requested to explore the feasibility of increasing the DC link capacitance to the extent possible so as to reduce such problems by higher energy storage capacity. Existing rating 6.75 mF (9x750 uF). | BHEL concluded that the capacitance is adequately sized for the application. Further BHEL has indicated Increased capacitance is resulting in higher short circuit current limits which is detrimental for the equipment. Hence, increase in capacitance is not envisaged. BHEL was once again requested to look into the possibility to increase the DC link capacitance and other related aspects. BHEL has to specifically intimate the solution considering all the parameters.

## Slide 64: Performance of M/s. BHEL make Traction Converter
SN | Item | Action plan | Remark
4. | Failure of Electronic Cards (VIU/DCU) | VIU: BHEL has provided snubber circuit across the relay contacts. DCU: Board was getting corrupted when access with diagnostic s/w version 2.7. | 77 card failed in 2018-19 (Apr-Dec) whereas 55 cards were failed in year 2017-18. In spite of taking the steps, the rate of failure is increasing. It seems that the steps are not effective and the problem needs to be taken afresh.

## Slide 65: Performance of M/s. BHEL make Traction Converter
SN | Item | Details | Remarks
5. | “Harmonic Filter contactor (8.1 /8.2) stuck on” problem | Re appearing of “Harmonic Filter contactor (8.1 /8.2) stuck on” problem. | Needs further investigation.
6. | Harmonic filter current high. | Harmonic Filter current is current 300 to 325 amp. Whereas in other make Traction Converter it is 150 to 180 amp. | BHEL may study the logic of filter operation of other make.
7. | Issue of “flashing of power cable” at gland area inside converter. | This issue has been reported by ELS/BRC. Other Railways may give feedback. | Railway to respond.

## Slide 66: Performance of M/s. BHEL make Traction Converter
SN | Item | Details
8. | DDS MSG remains Blank for speed sensor | DDS MSG from Speed Sensor of TM Remains Blank causing difficulty in detection of faulty TM.
9. | Power module Stucchi coupling failure | In all the cases Power module Stucchi spindle found jam due to spring inside got defective.

## Slide 67: Performance of M/s. BHEL make Traction Converter
SN | Item | Action plan | Remark
11. | Sludge formation in coolant circuit of BHEL make Traction converter even after flushing and changing the coolant causing pressure switch chocked. | It appears this is an issue of improper cleaning. | 

## Slide 68: BHEL make Auxiliary Converter
<number>

## Slide 69: BHEL make Auxiliary Converter (SHED WISE)
<number>

## Slide 70: Performance of M/s. BHEL make Aux. Converter
SN | Item | Action plan | Remark
1. | Inverter module failure | Assembly process reviewed to prevent damage of IGBT terminals in the module. Further, power-up issue in the AMC module shall be addressed with increased initializing current. . | SW ver. 188.1 with less sensitive di/dt monitoring (2 to 3 µs) has been uploaded and regular cut-in since Jan’2018. Power up issue in AMC module: Resistor value modified to optimize the initializing current and same implemented from May 2016. No improvement in the performance.
2. | Control rectifier module failure | Power-up issue in the AMC module by addressing increased initializing current. Common to Inverter, Controlled Rectifier and Battery charger | 

## Slide 71: Performance of M/s. BHEL make Aux. Converter
SN | Item | Action plan | Remark
3. | No DDS of BUR with BT make traction converter. | No DDS of BUR is being recorded other than life sign missing in Locos equipped with BT make Traction Converters. | Compatibility issue with BT make SR. BT and BHEL has modified the software to address the issue. Tested in loco no. 31943 at ELS/Katni. Firmware was updated and message getting logged. However, BHEL has not still started downloading the updated firmware.

## Slide 72: Performance of M/s. BHEL make Aux. Converter
SN | Item | Action plan | Remark
4. | Low BUR-2 frequency | Frequency of message TR-1 & 2 oil pressure not OK & Converter-1 & 2 Coolant pressure not OK is abnormally high. BUR-2 frequency at that moment is found 15 to 20 Hz. whereas, frequency of BUR-3 is 50 Hz in the back ground data. | Firm has indicated they have addressed the issue in software version -188.1. Railways to indicate if the problem is resolved in software version – 188.1.
5. | Main power off | Isolation of BUR1,2 & 3 due to Low/No OHE followed by Main power off as compared to other make Auxiliary converter. | 

## Slide 73: Performance of M/s. BHEL make Aux. Converter
SN | Item | Action plan | Remark
6. | Overheating of power cable terminal lug supporting stud | Overheating of power cable terminal lug supporting stud inside the BUR Box-1 & 2 due to bad conductivity between stud and hexagonal socket reported by ELS/GMO and ELS/BRC | Firm has stated that Brass studs have been made available to loco sheds. Very poor response of firm in BRC. Only 03 nos. locos out of 22 locos. Other Railways to give feedback.

## Slide 74: Performance of M/s. BHEL make Aux. Converter
SN | Item | Details | Remark
7. | Mismatch of Ramp up time | Mismatch of Ramp up time (16 sec) of BHEL make auxiliary converter with monitoring time (15 Sec) of BT make Traction Converter even in latest software version R-1240 causing several time message of ‘TFP oil pressure not OK’ and after 3 times this leads to “ Main Power Off”. | 

## Slide 75: Performance of M/s. BHEL make Aux. Converter
SN | Item | Details | Remark
8. | Contactor logic neither recorded in DDS nor in Aux. ACI card. | Isolation of Aux. Converter due to contactor logic neither recorded in DDS nor in Aux. ACI card. Only pop up message shown, so isolation of Aux. converter due to contactor mal operation could not be identified at shed. | 
9. | BUR 3 input current is having a variation of upto 20A between phases when Battery charger is in service. | Firm to look into. | 
10. | There is power supply breaker to battery charger processor card and when it fails loco shut down with message battery voltage less than 82 V. | Firm to look into. | 

## Slide 76: Performance of M/s. AAL make Aux. Converter
<number>

## Slide 77: Performance of M/s. AAL make Aux. Converter

## Slide 78: Performance of M/s. AAL make Aux. Converter (SHED WISE)

## Slide 79: Performance of M/s. AAL make Aux. Converter
SN | Item | Action plan | Remark
1 | Failure of PCB cards | Firm to give action plan | Firm to submit the action plan.
2. | Compatibility of the messages with other make converters | Issue to message incompatibility with BTIPL make traction converter. | Regular cut in of the Version 54 has been done.
3. | Software malfunctioning | Software malfunctioning cases increased. | Firm to submit the action plan.

## Slide 80: Other Important Issues
Development of facilities for full load testing & software testing at OEM’s premises.
Status of development of Composite Converter (TC+HLC) for WAP5 locos.
Progress of Push-Pull modification in WAP5 & WAP7 locomotives.

## Slide 81: Upgradation of WAP-5 to 6000 HP
<number>
Loco type |  | GZB | BRC | Total
GTO SR | Population | 43 | 40 | 83
 | Upgraded | 43 | 35 | 78
BHEL SR | Population | 32 | 17 | 49
 | Upgraded | 2 | 0 | 2
ABB SR | Population | 6 | 8 | 14
 | Upgraded | 5 | 2 | 7
BTIPL SR | Population | 1 | 0 | 1
 | Upgraded | 1 | 0 | 1
Medha SR | Population | 11 | 3 | 14
 | Upgraded | 8 | 0 | 8
CGL SR | Population | 0 | 0 | 0
 | Upgraded | 0 | 0 | 0
Total | Population | 93 | 68 | 161
 | Upgraded | 59 | 37 | 96

## Slide 82: Infrastructure needed for Maintenance of 3-Phase Locomotives (Position as on 31.01.2019)
Basic infrastructure
Test Setup
Other Facilities
Developmental items

## Slide 83: Basic infrastructure
SN | Item | AQ | BIA | CNB | BRC | HWH | GMO | GZB | KYN | KZJ | LGD | RPM | TATA | BNDM | TKD | LDH | WAT
1 | Loco Diagnostic System (LDS) – Defective/Total | 4/5 | 1/7 | 2/2 | 3/4 | 0/2 | 0/3 | 2/5 | 1/4 | 0/2 | 0/2 | 2/6 | 3/4 | N/A | 3/8 | 0/0 | 0/8
 | New windows based LDS | 2 | 3 | 1 | 3 | 4 | 4 | 1 | 3 | 1 | 3 | 1 | 3 | Yes | 3 | 2 | 3
2 | Set of Loop Boxes with Sub-D and Gimota Circular Connector | Yes | Yes | Yes | Yes* | Yes | Yes* | Yes* | Yes* | Yes | Yes | Yes | Yes | No | Yes | No | No
3 | Dedicated computers for storage of DDS | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
4 | System of interconnected electronic racks as TC/134 | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | No | Yes | No | Yes
* Partially available

## Slide 84: Test Setup Required in Maintenance Shed
Item | AQ | BIA | CNB | BRC | HWH | GMO | GZB | KYN | KZJ | LGD | RPM | TATA | BNDM | TKD | LDH | WAT
Testing of WRE Module as per SMI/261 | Yes | Yes | N/A | Yes | Yes | Yes | Yes | Yes | N/A | Yes | Yes | Yes | N/A | Yes | N/A | N/A
Testing of WRE gate unit card as per SMI/256 | Yes | Yes | N/A | Yes | Yes | Yes | Yes | Yes | N/A | Yes | Yes | Yes | N/A | Yes | N/A | N/A
Testing of SAP card as per SMI/260 | Yes | Yes | N/A | No | Yes | Yes | Yes | N/A | N/A | Yes | Yes | Yes | No | Yes | No | N/A
Testing Pressure Sensors | Yes | Yes | No | Yes | Yes | Yes | Yes | Yes | No | Yes | Yes | Yes | Yes | Yes | No | Yes

## Slide 85: Test Setup Required in Maintenance Shed
Item | AQ | BIA | CNB | BRC | HWH | GMO | GZB | KYN | KZJ | LGD | RPM | TATA | BNDM | TKD | LDH | WAT
Testing of Temp sensor as per SMI/260 | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | No | Yes | Yes | Yes | Yes | Yes | No | Yes
Testing of Speed Sensor | Yes | Yes | No | Yes | Yes | Yes | Yes | Yes | No | Yes | Yes | Yes | No | Yes | No | Yes
Testing of SR gate drive | Yes | Yes | No | Yes | Yes | Yes | Yes | N/A | N/A | Yes | Yes | Yes | N/A | Yes | N/A | N/A

## Slide 86
Other Facilities
Item | AQ | BIA | BRC | HWH | GMO | GZB | KYN | KZJ | LGD | RPM | TATA | BNDM | TKD | LDH | WAT
PCB handling and infrastructure for electronic lab | Yes | Yes | Yes | Yes | Yes | Yes | Yes | No | Yes | Yes | Yes | Yes & No resp. | Yes | No | Yes*
Industrial type of vacuum cleaner | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
Water Pressure jet for cleaning the radiator and air filters | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
Facility for warm water for cleaning of the filters | Yes | Yes | Yes | Yes | No | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | No | Yes
GTO valve set repair facilities as per RDSO SMI for the sheds which undertake the GTO valve set repair. | Yes | N/A | N/A | N/A | Yes | Yes expt clamping facility | N/A | N/A | Yes | N/A | N/A | N/A | Yes | N/A | N/A
Notes: <number>

## Slide 87: CRITICAL RAP OF 3-PHASE LOCOMOTIVES

## Slide 88: Position of One Time Important RAP
 |  | Replacement of EPROM after 6 years of service |  | Create low pressure zone by providing Baffle plates |  | Blocking leak holes in the Machine Room |  | Reed relay modification |  | Cab redundency modification | 
 | Shed | No. of Locos to be done | Cumulative up to date | No. of Locos to be done | Cumulative up to date | No. of Locos to be done | Cumulative up to date | No. of Locos to be done | Cumulative up to date | No. of Locos to be done | Cumulative up to date
CR | AQ | 100 | 53 | 199 | 199 | 199 | 199 | 169 | 169 | 166 | 120
CR | KYN | 0 | 0 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 64
ECoR | WAT | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ECR | GMO | 82 | 48 | 195 | 195 | 195 | 195 | 162 | 162 | 163 | 130
ER | HWH | 3 | 3 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25
NCR | CNB | 0 | 0 | 28 | 28 | 28 | 28 | 0 | 0 | 28 | 28
NR | GZB | 99 | 66 | 87 | 87 | 190 | 190 | 148 | 148 | 87 | 87
NR | LDH | 0 | 0 | 44 | 44 | 44 | 44 | 44 | 44 | 44 | 44
SCR | LGD | 103 | 62 | 207 | 207 | 207 | 207 | 164 | 164 | 164 | 158
SECR | BIA | 14 | 14 | 114 | 114 | 114 | 114 | 102 | 102 | 114 | 100
SER | TATA | 4 | 0 | 152 | 152 | 152 | 152 | 152 | 152 | 152 | 120
SR | RPM | 0 | 0 | 82 | 82 | 82 | 82 | 63 | 63 | 82 | 71
WCR | TKD | 39 | 39 | 168 | 168 | 168 | 168 | 168 | 168 | 119 | 71
WR | BRC | 9 | 4 | 90 | 90 | 90 | 90 | 83 | 83 | 90 | 64
Grand Total |  | 453 | 289 | 1455 | 1455 | 1558 | 1558 | 1344 | 1344 | 1298 | 1082

## Slide 89
Description | AQ | KYN | HWH | GMO | WAT | GZB | LDH | CNB | RPM | LGD | TATA | BIA | BRC | TKD | Total
Shifting of MCB-100 to HB-2 panel. (Ref : MS/0367) | 0 | 0 | 0 | 64 | 0 | 0 | 0 | 0 | 0 | 44 | 0 | 0 | 0 | 0 | 104
Rehabilitation of PCB cards (Ref : RDSO guideline no. ELG/2008/01, Rev. ‘1’ dated 13.08.09) | 54 | 0 | 6 | 34 | 0 | 52 | 0 | 0 | 0 | 66 | 8 | 30 | 12 | 34 | 296
Replacement of EPROM in locomotives after 6 years (Ref : TOT /RDSO guideline) | 47 | 0 | 0 | 34 | 0 | 33 | 0 | 0 | 0 | 41 | 8 | 30 | 8 | 0 | 201

## Slide 90
Description | AQ | KYN | HWH | GMO | WAT | GZB | LDH | CNB | RPM | LGD | TATA | BIA | BRC | TKD | Total
Modification in the SR cooling pump | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 16 | 0 | 0 | 0 | 18
Description | AQ | KYN | HWH | GMO | WAT | GZB | LDH | CNB | RPM | LGD | TATA | BIA | BRC | TKD | Total
Modified cooling radiators for SR. (Ref : RDSO L/N EL/11.5.5/5 dt. 15.02.10.) | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10
Description | AQ | KYN | HWH | GMO | WAT | GZB | LDH | CNB | RPM | LGD | TATA | BIA | BRC | TKD | Total
Roof clamp | 198 | 0 | 51 | 0 | 0 | 0 | 0 | 28 | 41 | 0 | 160 | 120 | 0 | 90 | 688

## Slide 91
Description | AQ | KYN | HWH | GMO | WAT | GZB | LDH | CNB | RPM | LGD | TATA | BIA | BRC | TKD | Total
KUC 153 A01 Power supply card of Auxiliary converter (Ref : Replacement of capacitors of KUC 153 A01 card after service life of 06 years.) | 24 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 59 | 8 | 0 | 11 | 0 | 104
Description | AQ | KYN | HWH | GMO | WAT | GZB | LDH | CNB | RPM | LGD | TATA | BIA | BRC | TKD | Total
Modified cooling radiators for SR. (Ref : RDSO L/N EL/11.5.5/5 dt. 15.02.10.) | 10 | 0 | 0 | 0 | 0 | 0 | 44 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 54

## Slide 92: Thanks !
<number>